Calculation of CO sensor resolution requirements for shipboard eddy covariance

The proposed instrument is commercially available from Los Gatos Research Inc. – their model DLT-100 fast CO and N2O analyzer. The method is off-axis integrated cavity output spectroscopy, and has proven to achieve very high precision in field tests with 1 second standard deviation levels of ~0.1-0.2 ppbv for both species.

1. Estimate of sea-air flux of CO

{from Bates et al., 1995}:

[CO] in summertime ocean surface waters of the South Pacific (45-60(S) ~ 2.6 nM, or (pCO ~ 2.3 (atm. From Sander 1999 (http://www.mpch-mainz.mpg.de/~sander/res/henry.html), the Henry's law constant for CO is 9x10-4 M atm-1. Then given a mean wind speed of 9 m/s, and a piston velocity of 4.8 m/d a reasonable flux of CO expected from the region is

this is equivalent to 2.6x10-3 in kinematic flux units of ppb ms-1.

2. Estimate resolution requirement for measurement such that instrumental noise is only 10% of the flux induced variations.

{from Rowe et al., in review}:

The resolution requirement, R, can be expressed as

where AP' is the "atmospheric parameter", which for slightly unstable conditions is right around 100 (their Fig. 2). For wind speeds of ~10 m/s, the friction velocity can be expected to be ~.35 m/s, so the sensor resolution needs to be

or formulated another way based on the air-sea disequilibrium pressure, (pCO, expected we can use their Eq. 29a

the CPc being their "chemical parameter" made up of the solubility, and the ratio of transfer to friction velocities. From their Fig. 3, its value for CO is 6.3x10-6. By this approach the requisite instrumental noise level is ~0.14 ppb.

According to tests outlined in Provencal et al. (2010, EGU poster) the 1 s precision of the LGR instrument is 0.14 ppbv for CO. Thus it appears that the technique should be able to measure realistic CO fluxes by eddy covariance with minimal error (~<20%) introduced by instrumental noise.

Nitrous oxide fluxes from the ocean are observed to be very similar in molar output to CO (1-30 (mol m-2d-1: Cornejo et al, 2007; Law & Ling, 2001), and therefore should require a similar resolution. Again according to LGR, the instrumental precision for N2O is even lower (.09 ppb in 1 s) and thus it should be possible to simultaneously measure N2O fluxes from the ocean.