FY2007 Add Task For

NOAA’s Climate Observations Program

High Resolution Climate Data From Research and Volunteer Observing Ships

New Task

Strategic Improvements in Ocean Observing System Wind Measurements:

Model Calculations of Flow Distortion Effects on Ship Anemometers

November 2006

Project Manager: C. W. Fairall, Chief of Weather and Climate Physics Branch

Physical Science Division

NOAA Earth System Research Laboratory, 325 Broadway, Boulder, CO 80305

303-497-3253 Chris.Fairall@noaa.gov

Finance Contact: Jo Novosel, 303-497-6588 Jo.Novosel@noaa.gov

Lab Director: William D. Neff

ADD TASK SUMMARY

This base project involves the measurement of direct high-resolution air-sea fluxes on one to two cruises per year and the development of a roving standard flux measuring system to be deployed on a series of NOAA and UNOLS research vessels to promote the improvement of climate-quality data from those platforms.  The project development is the result of a recent NOAA-sponsored workshop on high-resolution marine measurements which identified the need to more efficiently utilize research vessels, including realizing their potential for the highest quality data and their potential to provide more direct and comprehensive observations. Buoys and VOS systems are required to operate virtually unattended for months, so considerations of practical issues (e.g., power availability, instrument ruggedness, or safe access) are balanced against inherent sensor accuracy and optimal sensor placement. Such information can be provided by suitably equipped research vessels (R/V). Thus, the accuracy of buoy and VOS observations must be improved and supplemented with high-quality, high time resolution measurements from the US R/V fleet (which is presently underutilized).

With the advent of modern and accurate sonic anemometers, measurements of wind speed from ships are compromised principally through flow distortion by the structure.  Mounting locations for anemometers are a compromise between accessibility for maintenance and reducing flow distortion errors.  Corrections for flow distortion are now made using Computational Fluid Dynamics (CFD) codes run on numerical models [Moat BI, Yelland MJ, Pascal RW, et al., An overview of the airflow distortion at anemometer sites on ships 
INTERNATIONAL JOURNAL OF CLIMATOLOGY 25 (7): 997-1006 JUN 15 2005] of simplified ship structure (see Figure 1 for an example for the NOAA Ship Ronald H. Brown).  In the past, a CFD model runs were contracted to commercial firms and were so expensive it was only practical to perform the calculations at one or two relative wind direction for a specific ship.  In recent years it has become feasible to purchase the CFD code and run them in house.   Corrections for flow distortion will result in significant direct improvements in the accuracy of wind observations from R/V and VOS with additional benefits to buoy observations through the intercomparison process.

Following the recommendations of the 1st GOSUD/SAMOS Workshop (Boulder, CO, 2-4 May 2006), Shawn Smith (FSU) is planning to submit a proposal to NSF to develop this capability with C. Fairall (ESRL) as a technical collaborator.  The first ship to be examined will be the planned Alaskan Arctic Research Vessel (AARV - University of Alaska).  NSF cannot fund NOAA laboratories, so we seek OCO funds for this work as an additional task to the ESRL project.  The plan is to transition this capability to NOAA OMAO for future applications in the design and construction of NOAA R/V’s.

For this project, we propose to obtain a commercial version of a CFD code (GERRIS) and develop the capability to run the code at numerous wind speeds, relative wind directions, and represent the results in a simplified distortion parameterization that can be routinely applied to correct ship’s anemometer for better true wind speed estimates.  The plan is to acquire the software and develop the capability to apply it to any ship.  In the first year we will duplicate the earlier CFD results for the Ronald H. Brown.  In the second year, apply the model to the AARV, and in the third year generalize the model for running with UNOLS and NOAA ships.

Figure 1. CFD simulation of wind flow around NOAA Ship Ronald H. Brown.  Positions of two sensors are shown as black dots on particle trajectories that pass through them, showing the flow deflected sideways and upward at each site. Other trajectories originate 100 m upwind on the centreline of the ship, at heights of 5, 7, 9, and 15 m above the sea surface. The colours represent wind speed and scale from 5 to 15 ms-1. Courtesy Ben Moat.

FY2007 PLAN

The major effort in FY07 will be acquisition of the GERRIS code and the installation at ESRL.  This will be done in consultation with a representative from the parent company in New Zealand.  R. J. Hill (ESRL/CIRES) will be responsible for running the model.  The numerical paneling for the Ronald H. Brown will be obtained from Ben Moat and the original VECTIS results at two relative wind angles will be duplicated.  Once that is successful, the code will be run for 10 different relative wind directions and a report written.

FY2007 BUDGET SUMMARY

The total ESRL request to OCO for this ADD TASK project is k$52 in FY2007.  This is one month of salary for C. Fairall, one month for R. J. Hill, and travel funds.  The OCO budget breakdown is as follows

Salaries, including overhead			  36

Travel						    3

IT support					    6

Admin support				    7

See attached budget sheet for details.

DELIVERABLES

*Report on flow distortion model results for NOAA Ship Ronald H. Brown.