FY2011 Work Plan For

NOAA’s Climate Observations Program

High Resolution Climate Data from Research and Volunteer Observing Ships

December 2010

Period covered by this workplan: Oct 1, 2010 - Sept 30, 2011

Project Manager: C. W. Fairall, Chief of Weather and Climate Physics Branch

Physical Science Division

NOAA Earth System Research Laboratory, 325 Broadway, Boulder, CO 80305

303-497-3253 Chris.Fairall@noaa.gov

Finance Contact: Jo Novosel, 303-497-6588 Jo.Novosel@noaa.gov

Division Director: William D. Neff

PROJECT SUMMARY

This project focuses on the measurement of direct high-resolution air-sea fluxes on one to two cruises per year and the development and deployment of a roving standard flux measuring system to be deployed on a series of NOAA and UNOLS research vessels to promote the improvement of climate-quality data from those platforms.  An adjunct task is maintenance and operation of the C-band scanning Doppler radar and the stabilized wind profiling radar on the NOAA ship Ronald H. Brown.  The wind profiler is no longer functional on the Ronald H. Brown, and costs to refurbish the system may be prohibitive.  Because buoys and most ships and satellites rely on bulk methods to estimate fluxes, another aspect of this project is the use of direct measurements to improve the NOAA/COARE bulk flux algorithm.  Originally one cruise was the annual TAO buoy tending cruise to 95W and 110 W on the Ronald Brown, but after several years participation in the TAO cruise was discontinued in favor of participation in the annual cruise to the equatorial Atlantic Ocean with NOAA/AOML as part of the African Multidisciplinary Monsoon Analyses (AMMA) and Saharan Dust studies (now part of the PIRATA Northeast Extension; PNE).  In 2000, a second cruise was added to participate in the annual turn-around of the Stratus climate buoy at 20S 85W.  Due to the success of the Stratus cruise participation and the fruitful collaboration with WHOI and in order to maintain a more relevant connection with the climate reference buoys, ESRL now participates in the annual turn-around of the Northwest Tropical Atlantic Station (NTAS) and in the annual turn-around of the WHOI Hawaii Ocean Time Series (WHOTS).

A full suite of direct, inertial-dissipation, and bulk turbulent fluxes are measured along with IR and solar radiative fluxes, precipitation, and associated bulk meteorological properties. This effort represents a partial transition of research from the OGP CLIVAR PACS program to operations under the Climate Observations Division (COD).

The project development is the result of a NOAA-sponsored workshop on high-resolution marine measurements (Smith et al., 2003, Report and Recommendations from the Workshop on High-Resolution Marine Meteorology, COAPS Report 03-01, Florida State University, pp38) which identified three important issues with the planned NOAA air-sea observation system: 1) the need for a data quality assurance program to firmly establish that the observations meet the accuracy requirements, 2) the need for observations at high time resolution (about 1 minute), 3) and the need to more efficiently utilize research vessels, including realizing their potential for the highest quality data and their potential to provide more direct and comprehensive observations.  For seasonal time scales, the net air-sea flux (sum of 5 flux components) must be constrained within 10 Wm-2.  Buoys and VOS systems are required to operate virtually unattended for months, so considerations of practical issues (e.g., power availability, instrument ruggedness, or safe access) are balanced against inherent sensor accuracy and optimal sensor placement.  As discussed above, an important function of the in situ measurements is to provide validation data to improve NWP and satellite flux fields.  High time resolution and more direct observations are invaluable for interpreting surface flux measurements and diagnosing the source of disagreements; such information can be provided by suitably equipped research vessels (R/V). Thus, the accuracy of buoy and VOS observations must be improved and supplemented with high-quality, high time resolution measurements from the US R/V fleet (which is presently underutilized).  The necessity for both high time resolution and high accuracy places extreme demands on measurements because some sources of error (such as the effect of ship flow distortion on wind speed) tend to average out over a large sample.  To accomplish this task will require a careful intercomparison program to provide traceability of buoy, VOS, and R/V accuracy to a set of standards.

This project directly addresses the need for accurate measures of air-sea exchange in the  Program Plan for Building a Sustained Ocean Observing System for Climate (Sections 5.2-5.4), and it is a joint effort by ESRL and Dr. Robert Weller of the Woods Hole Oceanographic Institution (WHOI).  The ESRL Air-Sea Interaction Group website can be found at: http://www.esrl.noaa.gov/psd/psd3/air-sea/. ESRL also cooperates with Dr. Frank Bradley (CSIRO, Canberra Australia) on precipitation and radiative flux observations, Dr. Meghan Cronin (PMEL) on buoy-ship intercomparisons and climate variability analysis, and Dr. Wade McGillis (Univ. Columbia) on trace gas fluxes.  A project website has been developed (High Resolution Climate Observations http://www.esrl.noaa.gov/psd/psd3/air-sea/oceanobs/ ).  An associated website (http://www.esrl.noaa.gov/psd/psd3/wgsf/ ) contains a handbook on best practices for flux measurements plus a database of high-resolution flux data.  This work will be closely monitored by the WCRP Working Group on Surface Fluxes (WGSF) which is chaired by C. Fairall.  This will give the project high visibility in the CLIVAR, GEWEX, and SOLAS programs.  This project will be managed in cooperation with JCOMM (and other) panels as per instructions of David Goodrich.

This project directly addresses the Climate Observation and Monitoring Program deliverables for improved observations of Air-Sea Exchange, and for accurate measurement of Sea Surface Temperature.

FY2011 PLANS

FY11 figures to be a challenging year for the project, with multiple deployments of the ESRL turbulent flux measurement system and the ESRL roving flux standard.  Major efforts in FY11 will be execution of the Stratus climate reference cruise on the R/V Moana Wave in April from Arica, Chile, one roving standard deployment on the R/V Kilo Moana for the WHOTS buoy redeployment cruise, and preparing deployment of the systems for a major multi-leg cruise on the R/V Revelle at the end of the fiscal year.  This interagency-funded, multi-platform international campaign is part of the DYNAMO/CINDY project in the Indian Ocean. Given unexpected delays in the schedule of the Ronald H. Brown, ESRL was not able to participate in the NTAS buoy turn-around cruise in December 2010. We continue to coordinate with the SAMOS project for calibration of observational systems on board UNOLS vessels.

For the Ronald Brown radar systems project, some work is planned this year for the C-Band radar upgrade.  Foremost is the integration of the ship’s new navigation system into the radar system processing stream. In addition, a new hydrator will be installed for the radar waveguide.  The Vaisala (formerly SIGMET) IRIS software licenses and maintenance will also need to be continued (this is k$9 per year.  The Ronald Brown wind profiler has been removed from the ship, and ESRL is investigating possibilities for upgrading the hardware and software for this radar system.

We will continue our cooperation with Dr. Huai-Min Zhang of NOAA NCDC on the Surface Flux Analysis (SURFA) project (http://www.ncdc.noaa.gov/oa/rsad/air-sea/surfa.html).  ESRL has downloaded from the SURFA website surface flux fields from the ECMWF and the German DWD operational global forecast models.  We have performed preliminary comparisons of these model outputs with the in situ observations from the Stratus buoy.  In FY11 we are planning a comprehensive study of SURFA data with five Oceansites buoy locations; this is a cooperation with Andy Brown of the UK Met Office and Huai-min Zhang of NCDC.

Of high relevance to this project, ESRL has secured independent funding to work with Sonoma Technology Incorporated (STI) and the Louisiana State University (LSU) to develop an exploratory “test bed” for high quality turbulent flux measurements from an oil platform in the Gulf of Mexico.  Some of the equipment and expertise from this project will be utilized to develop the technology and experience to operate observational flux systems from this remote platform (12km offshore).  It is anticipated that this technological development will provide much-needed data coverage in an under-utilized region so critical to the climate and weather of the continental USA.

In addition, ESRL is looking forward to the implementation stages of the Ocean Observatories Initiative (OOI) as our work with the roving flux standard may present a highly valuable resource for validation of the buoy instrumentation.  We envision ESRL’s role in much in the same manner as our fruitful collaborations with the group at WHOI in the climate reference buoy turn-around cruises for Stratus, WHOTS, and NTAS.

ESRL is working to coordinate deployment of the roving flux standard on a NOAA Arctic fisheries research vessel (Oscar Dyson) in order to develop the capability for work in high wind, high sea regions in anticipation of potential deployment of the systems on the new UNOLS research vessel at the University of Alaska, Fairbanks (R/V Sikuliaq).

Outreach efforts will continue primarily through the CIRES Outreach Office projects, including participation by the PI and other members of the ESRL Air-Sea Interaction Group in the COSEE-funded annual workshop for local earth science teachers.

FY2011 BUDGET SUMMARY

The total ESRL request to OCO for this project is k$360 in FY2011.  This is augmented by k$29 in PI salary and about 50 k$ in other ESRL base contributions (salary, travel, etc).  The OCO budget breakdown is as follows

Salaries, including overhead			156k

Capital equipment				  40k

Software contract				  10k

Travel						  25k

Shipping					  40k

Supplies					    7k

Sondes					  	  20k

Misc						    6k

IT support					  26k

Admin support				  31k

The breakdown of this budget is as follows: operations - 70%, data management - 10%, R&D - 20%.  The program supports 0.60 federal FTE and 0.375 non Federal FTE; 0.30 Fed FTE are devoted to the project but not funded by it.  See attached budget page for details.

DELIVERABLES

* Stratus buoy turn-around cruise in collaboration with WHOI on the R/V Moana Wave, April 2011.  Note that the ship is a private vessel, chartered by NOAA for the buoy turn-around, and thus is not a participant in the SAMOS data sharing project.

* WHOTS buoy turn-around cruise in collaboration with WHOI on the R/V Kilo Moana in July 2011.

* Prepare and ship the ESRL roving flux standard for deployment on the R/V Revelle for the DYNAMO cruises September-November 2011

* Process and post flux data sets from 2009 and 2010 deployments to the ESRL/PSD data archive

* Finalize and publish reports (most likely as NOAA Technical Memos) from previous deployments of the roving flux standard on the R/V Kilo Moana (WHOTS), USCG Icebreaker Healy and the R/V Knorr (ICEALOT).

* Prepare a joint paper with WHOI on the intercomparison of ship-based and buoy fluxes at WHOI Stratus buoy site.

* Investigate the intercomparison of SURFA model output data with five WHOI and PMEL buoys and ESRL R/V observations, and prepare a presentation for the AGU and/or AMS conferences.

* Visit CSIRO in Canberra to work on an intercomparison of the suite of radiometers deployed over the past several years on the ships plus land-based calibrations in Boulder and Woods Hole.  This paper will be in collaboration with Dr. Frank Bradley at CSIRO and Dr. Weller at WHOI.