MONTHLY REPORT

of the instrument park HMO Tiksi for February 2014

CRN- fans working with increased/higher temperatures

BSRN- tracker working with increased/higher temperatures; requires additional heating to avoid similar situations

02/25/14 at 07:00 – 15:30 power off because of work on diesel

Cimel- re-installed several times, chaotic motion, the sun does not catch

Aethalometer - dependent 02/24/14 of Kondratiev VO 25.02.14 g restarted device

but judging by the complaints AARI data from the instrument are not available. Restarted computer, but did not help. Request instructions to restart the device itself.

HMO programmers left. (Sinjakov resigned, Kondratiev two months on vacation).

Sincerely Volkov E.

МЕСЯЧНЫЙ ОТЧЕТ

работы приборного парка ГМО Тикси за февраль 2014 г.

CRN- при повышении температуры воздуха заработали вентиляторы.

BSRN- при повышении температуры воздуха заработал треккер.

Необходим дополнительный обогрев во избежание аналогичных ситуаций.

25.02.14 г. с 07-00 до 15-30 отключение э/энергии (работа на дизеле)

Cimel –несколько раз переустанавливали, движение хаотичное,солнце не ловит.

Аэталометр-завис 24.02.14 г. Кондратьев В.О. 25.02.14 г перезапускал прибор,

но судя по рекламации ААНИИ данные с прибора не поступают.

Программистов в ГМО не осталось.(Синяков уволился,Кондратьев на два месяца

в отпуске). Компьютер аэталометра перезапустил.Просьба скинуть инструкцию по перезапуску самого прибора.

С уважением  Волков Е.