FMI's Tiksi greenhouse gas concentration and flux measurement system data formats

There are three main measurement systems running on a single industrial PC under Linux/KDE operating system. The programs are written in python programming language, and they are run directly from the source code, i.e. program source is visible/editable at the station. These systems are:

1. CH4/CO2/H2O micrometeorological flux measurement system

2. Supporting meteorological observations for the flux system

3. CH4/CO2/H2O concentration measurement system

All the systems produce ASCII (text) data files, and in addition rotating text log files for identifying/solving possible system problems. Data is stored as 30 minute averages for the system 2 and one minute means for the system 3, and at 10 Hz (10 readings/second) for the flux system. The flux system data files are large, and preliminary results are calculated in the station computer every 30 minutes. These data/result files are sent/fetched via internet automatically daily. In addition of transferring above mentioned files (preferably via rsync, FTP is also useable), a possibility to get a remote connection to the computer (telnet/ssh and/or vnc) would be important in case of system malfunctions. The measurement systems (computers) at the station should also have a common time server, to which all the system should syncronise their time-of day clocks. The computer creates also a file Tiksi_FMI_logbook.txt, which contains system error messages.

1. Data from the flux measurement system

A raw data files contain 30 minutes (one measuring period) of data at 10 Hz, and they are named as yyyymmddhhmm_tiksi_flux.RAW, where yyyy is the year, mm is the month, dd is the day, hh hour and mm minute. The files are space separated text files with each data line containing:

Parameter			Short name	Sensor/Source	Format

Data read hhmmss.t (in UTC)	time		Computer clock		%08.2f

wind speed in u direction 		u [cm s-1] 	Metek anemometer 	%d

wind speed in v direction 		v [cm s-1] 	Metek anemometer 	%d

wind speed in w direction 		w [cm s-1] 	Metek anemometer 	%d

sonic temperature 		Ts [C] 		Metek anemometer 	%d

CO2 concentration 		CO2 [ppm] 	Licor 			%.2f

H2O concentration 		H2O [mmol mol-1] Licor 			%.3f

Licor temperature 		LiT [C] 		Licor 			%.2f

Licor pressure 			LiP [kPa] 	Licor 			%.2f

CH4 concentration 		CH4 [ppm] 	LGR 			%.4f

LosGatos cell pressure 		CH4 [kPa] 	LGR 			%.3f

LosGatos cell temperature		CH4 [C] 	LGR 			%.3f

LosGatos ring down time 		CH4 [us] 	LGR 			%.6f

The format for each parameter is expressed with format characters used e.g. in C and python. The amount of uncompressed ASCII data is ca. 1500 kB/file, or 70 MB/day (24 hours). This data is automatically compressed (zipped) every day to a daily file named as yyyymmdd_Tiksi_flux.zip , where yyyy is the year, mm is the month and dd is the day. The size of this file is ca. 18 MB. In addition the program writes a second file in csv (comma separated values in ASCII, i.e. text) format consisting 30-min averages of additional data read from LGR:

Parameter 			Short name 	Sensor/Source Format

Period end date and time in UTC 	endDT [UTC] 	Computer clock yyyy-mm-dd hh:mm

Average LGR cell pressure 	p [torr] 		LGR 		%.2f

Minimum LGR cell pressure 	min(p) [torr] 	LGR 		%.2f

Maximum LGR cell pressure 	max(p) [torr] 	LGR 		%.2f

Average LGR cell temperature 	T [C] 		LGR 		%.2f

Minimum LGR cell temperature 	min(T) [C] 	LGR 		%.2f

Maximum LGR cell temperature 	max(T) [C] 	LGR 		%.2f

Average LGR mirror time 1	mt1 [us] 	LGR 		%.2f

Minimum LGR mirror time 1	min(mt1) [us] 	LGR 		%.2f

Maximum LGR mirror time 1	max(mt1) [us] 	LGR 		%.2f

Average LGR mirror time 	2	mt2 [us] 	LGR 		%.2f

Minimum LGR mirror time 2	min(mt2) [us] 	LGR 		%.2f

Maximum LGR mirror time 2	max(mt2) [us] 	LGR 		%.2f

These two raw data files are not routinely sent from Tiksi. Only the following 30 min average flux data file is normally sent from Tiksi.

File name is in format Tiksi_flux_LGR_yyyymmdd.csv, where yyyy is the year, mm month and dd day. The first line in every file is a header line consisting of comma separated short names enclosed in double quotation marks:

Data starts from line 2. The amount of uncompressed ASCII data is ca. 4 kB/day. After each measuring period (30 minutes) preliminary results are calculated and appended to a file named as Tiksi_flux_res_yyyymmdd.csv:

Parameter 				Short name 				Format

Period end date and time time in UTC 	period end [UTC] 		yyyy-mm-dd hh:mm

Average wind direction 			wind dir [deg] 		Metek		%d

Average wind speed 			wind speed [m/s] 		Metek		%.3f

Friction velocity 				friction velocity [m/s] 	Metek		%.3f

Average wind u component velocity 	avg(u) [m/s] 		Metek		%.3f

Average wind v component velocity 	avg(v) [m/s] 		Metek		%.3f

Average wind w component velocity 	avg(w) [m s-1] 		Metek		%.3f

Average sonic temperature 		avg(Ts) [C] 		Metek		%.3f

Average CO2 concentration 		avg(CO2) [ppm] 		Licor		%.3f

Average H2O concentration 		avg(H2O) [mmol mol-1] 	Licor		%.3f

Average Licor cell temperature 		avg(Lit) [C]		Licor		%.3f

Average Licor cell pressure 		avg(LiP [kPa] 		Licor		%.3f

Average CH4 concentration 		avg(CH4 [ppm] 		LosGatos	%.3f

Average LosGatos cell pressure 		avg(CH4p) [torr]		LosGatos	%.3f

Average LosGatos cell temperature 	avg(CH4t) [C]		LosGatos	%.3f

Average LosGatos ring down time 		avg(CH4mt) [us] 		LosGatos	%.3f

CO2 mass mixing ratio, dry air 		avg(s) [ug(CO2) g-1(dry air)] 		%.3f

H2O mass mixing ratio, dry air 		avg(q) [mg(H2O) g-1(dry air)] 		%.3f

CO2 mass mixing ratio, moist air 		avg(S) [ug(CO2) g-1(moist air)] 		%.3f

H2O mass mixing ratio, moist air 		avg(Q) [mg(H2O) g-1(moist air)] 		%.3f

Average wind component u variance 	<u'u'> [m2 s-2] 				%.3e

Average wind component v variance 	<v'v'> [m2 s-2] 				%.3e

Average wind component w variance 	<w'w'> [m2 s-2] 				%.3e

Average sonic temperature variance 	<Ts'Ts'> [K2] 				%.3e

Average CO2 concentration variance 	<CO2'CO2'> [ppm2] 			%.3e

Average H2O concentration variance 	<H2O'H2O'> [umol2 mol-2] 		%.3e

Average Licor cell temperature variance 	<Ts'Ts'> [K2] 				%.3e

Average Licor cell pressure variance 	<LiP'LiP'> [kPa2]			%.3e

Average CH4 concentration variance 	<CH4'CH4'> [ppm2] 			%.3e

Average LosGatos cell pressure variance 	<CH4p'CH4p'> [kPa2]			%.3e

Average LosGatos cell temperature variance	<CH4t'CH4t'> [K2]			%.3e

Average LosGatos ring down time variance 	<CH4mt'CH4mt'> [us2]			%.3e

Avarege s variance 			<s's'> [ug2 g-2] 				%.3e

Avarege q variance			 <q'q'> [mg2 g-2] 			%.3e

Avarege S variance 			<S'S'> [ug2 g-2] 				%.3e

Avarege Q variance 			<Q'Q'> [mg2 g-2] 			%.3e

Wind w and sonic T covariance 		w'Ts' [K m s-1] 				%.3e

Wind w and CO2 concentration covariance 	w'CO2' [ppm m s-1] 			%.3e

Wind w and H2O concentration covariance 	w'H2O' [ppm m s-1] 			%.3e

Wind w and Licor temperature covariance 	w'LiT' [K m s-1]	 			%.3e

Wind w and Licor pressure covariance 	w'LiP' [kPa m s-1] 			%.3e

Wind w and LosGatos pressure covariance 	w'CH4p' [torr m s-1] 			%.3e

Wind w and LosGatos temperature covariance w'CH4t' [K m s-1]			%.3e

Wind w and LosGatos ringdowntime covariance w'CH4mt' [us m s-1] 			%.3e

Wind w and s covariance 			w's' [ug g-1 m s-1] 			%.3e

Wind w and q covariance 			w'q' [mg g-1 m s-1] 			%.3e

Wind w and S covariance 			w'S' [ug g-1 m s-1] 			%.3e

Wind w and Q covariance 			w'Q' [mg g-1 m s-1] 			%.3e

Number of data records (lines) 		# data rec 				%d

Number of filtered data records 		# filt. data rec 				%d

Lag for u component 			lag(u) 					%d

Lag for v component 			lag(v) 					%d

Lag for w component 			lag(w) 					%d

Lag for T component 			lag(Ts) 					%d

Lag for CO2 				lag(CO2) 				%d

Lag for H2O 				lag(H2O) 				%d

Lag for Licor temperature (always 0) 	lag(Lit) 					0

Lag for Licor pressurere (always 0) 	lag(LiP) 					0

Lag for CH4 				lag(CH4) 				%d

Lag for LosGatos pressurere (always 0) 	lag(CH4p) 				0

Lag for LosGatos temperature (always 0) 	lag(CH4t) 				0

Lag for LosGatos ringdowntime (always 0) 	lag(CH4mt) 				0

Lag for s (always 0) 			lag(s) 					0

Lag for q (always 0) 			lag(q) 					0

Lag for S (always 0) 			lag(S) 					0

Lag for Q (always 0) 			lag(Q)					0

Average temperature of air			 <Ta>-To [C] 				%.3f

Density of air 				<density>/1000 [kg m-3] 			%.3f

CO2 mass flux density 			Fs/1000 [mg m-2 s-1] 			%.3e

CO2 mole flux density 			Fs/Mc [umol m-2 s-1] 			%.3e

Density correction of CO2 flux 		dFs/1000 [mg m-2 s-1] 			%.3e

H2O mass flux density 			Fq/1000 [g m-2 s-1] 			%.3e

H2O mole flux density 			Fq/Mw [mmol m-2 s-1] 			%.3e

Evaporation flux 				3600*Fq/1e6 [mm h-1] 			%.3e

Density correction of H2O flux 		dFq/1000 [g m-2 s-1] 			%.3e

Latent heat flux 				FL [W m-2] 				%.3e

Webb corrected CO2 flux 			FSW [mg m-2 s-1] 			%.3e

Webb corrected H2O flux 			FQW [mg m-2 s-1] 			%.3e

Vapour pressure deficit 			VPD/100 [hPa] 				%.3e

Relative humidity 			100*RH [%] 				%.3e

Buoyancy flux 				B [K m s-1] 				%.3e

Sensible heat flux 			FH [W m-2] 				%.3e

Momentum flux 				FM [N m-2] 				%.3e

Inverse Obukhov length 			L-1 [m-1] 				%.3e

Friction velocity 2 			ustar2 [m s-1] 				%.3f

Minimum CO2 concentration 		min(CO2) [ppm] 				%.2f

Maximum CO2 concentration 		max(CO2) [ppm] 			%.2f

CO2 average(last 30s) - average(first 30s) 	CO2 avg(last 30s)-avg(first 30s) [ppm] 	%.2f

Rotation angle 1 				phi 					%.3e

Rotation angle 2 				psi 					%.3e

u* stationarity 				(5minmean-halfh)/halfh (u*)		%.3e

mod u* stationarity 			abs(dev(5minmean)/halfh) (u*)		%.3e

Sensible heat flux stationarity 		(5minmean-halfh)/halfh (w’Ts’)	%.3e

mod sensible heat flux stationarity 		abs(dev(5minmean)/halfh) (w’Ts’)		%.3e

CO2 flux stationarity 			(5minmean-halfh)/halfh (w’CO2’)		%.3e

mod CO2 flux stationarity 			abs(dev(5minmean)/halfh) (w’CO2’)	%.3e

H2O flux stationarity 			(5minmean-halfh)/halfh (w’H2O’)		%.3e

mod H2O flux stationarity 		abs(dev(5minmean)/halfh) (w’H2O’)%.3e

CH4 flux stationarity 			(5minmean-halfh)/halfh (w’CH4’)		%.3e

mod CH4 flux stationarity 			abs(dev(5minmean)/halfh) (w’CH4’)	%.3e

CH4p flux stationarity 			(5minmean-halfh)/halfh (w’CH4p’)		%.3e

mod CH4p flux stationarity 		abs(dev(5minmean)/halfh) (w’CH4p’)	%.3e

CH4t flux stationarity 			(5minmean-halfh)/halfh (w’CH4’t)		%.3e

mod CH4t flux stationarity 		abs(dev(5minmean)/halfh) (w’CH4’t)	%.3e

CH4mt flux stationarity 			(5minmean-halfh)/halfh (w’CH4mt’)	%.3e

mod CH4mt flux stationarity 		abs(dev(5minmean)/halfh) (w’CH4mt’)	%.3e

Lag-average for CO2			lagq(CO2) 				%d

Lag-average for H2O 			lag(H2O) 				%d

Lag-average for CH4 			lag(CH4) 				%d

2. Data from the meteorological measurement system

The system writes two daily csv files which contain 30 min statistics calculated from one minute mean data. The files are named as tiLog_soil_yyyymmdd.csv and tiLog_air_yyyymmdd.csv:

The file tiLog_soil_yyyymmdd.csv

Parameter 			Short name 		Sensor/Source 	Format

Date and time in UTC, start minute Period start 		Computer clock 	dd.mm.yyyy hh:mm

Soil temperature -2cm moss	avg(SoilT-2 moss (C))		Pt100 		%.2f

Soil temperature -5cm		avg(SoilT-5 (C))			Pt100 		%.2f

Soil temperature -10cm		avg(SoilT-10 (C))		Pt100 		%.2f

Soil temperature -20cm		avg(SoilT-20 (C))		Pt100 		%.2f

Soil temperature -30cm  		avg(SoilT-30 (C))		Pt100 		%.2f

Soil temperature -40cm		avg(SoilT-40 (C))		Pt100 		%.2f

Soil surface temperature		avg(SoilTsurf (C))		Pt100 		%.2f

Soil humidity -20cm		avg(SoilHum -20 (V))		Delta-T		%.3f

Soil humidity -5cm		avg(SoilHum -5 (V))	 	Delta-T		%.3f

Soil heat flux -7cm		avg(SoilHeatFlux (uV))		Heat flux plate	%.2f

Air pressure			avg(p (mbar))			Pressure sensor	%.1f

Following columns have 30-min minimum,  maximum, standard deviation and median for all above parameters.

tiLog_air_yyyymmdd.csv

Parameter 			Short name 		Sensor/Source 	Format

Date and time in UTC, start minute Period start 		Computer clock 	yyyy-mm-dd hh:mm

Air temperature 			avg(Temp (C))		Vaisala Pt100 			%.2f

Relative air humidity 		avg(RH(%))		Vaisala Humicap HMD45D 	%.1f

Photosynthetically active radiation 	avg(PPFD (umol/m2/s)) 	Kipp&Zonen PAR-LITE 		%.1f

PPFDeflected from ground1	avg(PPFDrefl (umol/m2/s)) Kipp&Zonen PAR-LITE 	%.1f

PPFDeflected from ground2	avg(PPFDreflDry (umol/m2/s)) no sensor, no measurement	%.1f

Global radiation 			avg(Glob (W m-2) 	Kipp&Zonen CMP3 		%.1f

Reflected global radiation 		avg(GlobRefl (W m-2) 	Kipp&Zonen CMP3		%.1f

Net radiation 			NetRad (W m-2) 		Kipp&Zonen NR-LITE 		%.1f

Cabin temperature 		avg(CabinTemp (C))	Pt100 				%.2f

Following columns have 30-min minimum,  maximum, standard deviation and median for all above parameters.

The first line in every file is a header line containing comma separated short names enclosed in double quotation marks. Data starts from line 2. The amount of uncompressed ASCII data is ca. 500 kB/day.

3. Data from the concentration measurement system

The system write daily csv files which contain one minute mean data. The parameters are mostly internal diagnostic data of the system. The files are named as Tiksi_conc_G2301_yyyymmdd.csv, and they are in csv format:

Parameter 				Short name 	Sensor/Source Format

Date and time in UTC, start minute star	startDT [UTC] 	Computer clock 	yyyy-mm-dd hh:mm:ss

Valve positions 				vpos		Relay module 			%d

CH4 concentration 			CH4 [ppm] 	Picarro 2301 			%.5f

CH4 concentration standard deviation	stdev(CH4) [ppm] Calculated by the program 	%.5f

CO2 concentration 			CO2 [ppm]	Picarro 2301			%.3f

CO2 concentration standard deviation 	stdev(CO2) [ppm] Calculated by the program 	%.3f

H2O concentration 			H2O_reported [%]Picarro 2301			%.4f

H2O concentration standard deviation 	stdev(H2O_reported [%]) Calculated by the program 	%.4f

Picarro cell pressure 			CavityPressure [torr] Picarro 2301			%.3f

Picarro cell temperature 			CavityTemp [C]	Picarro 2301			%.3f

Picarro outlet valve 			OutletValve	Picarro 2301			%.2f

CH4 concentration in dry air		CH4_dry [ppm]	Picarro 2301			%.5f

CO2 concentration in dry air		CO2_dry [ppm]	Picarro 2301			%.3f

Picarro cell temperature 			DasTemp [C]	Picarro 2301			%.3f

Picarro Etalon temperature			EtalonTemp [C]	Picarro 2301			%.3f

Picarro Warm Box temperature		WarmBoxTemp [C]Picarro 2301			%.3f

MPValve Position			MPVPosition 	Picarro 2301			%.0f

Precooler temperature 			T_ECpre [C] M&C EC30 air dryer 			%.2f

Cooler stage 1 temperature 		T_EC1 [C] 	M&C EC30 air dryer 		%.2f

Cooler stage 2 temperature 		T_EC2 [C] 	M&C EC30 air dryer 		%.2f

Inlet line pressure 			p_inlet [hPa] 	Pressure transmitter 		%.0f

Pressure before LGR 			p_in [hPa] 	Pressure transmitter 		%.0f

Pressure after LGR 			p_out [hPa]	Pressure transmitter 		%.0f

Inlet line sample temperature 		T_inlet [C] 	T/RH sensor module 		%.1f

Inlet line sample relative humidity		RH_inlet [%] 	T/RH sensor module 		%.1f

Inlet line sample dew point temp. 		dwpt_inlet [C] 	Calculated (computer) 		%.1f

Vent air temperature 			T_vent [C]	T/RH sensor module 		%.1f

Vent air relative humidity 			RH_vent [%] 	T/RH sensor module 		%.1f

Vent air dew point temperature 		dwpt_vent [C] 	Calculated (computer) 		%.1f

Vent air flow 				flow_vent [l min-1] flow sensor 			%.2f

Sample air flow 				flow_inlet [l min-1] flow sensor 			%.2f

Sample air dew point temperature 		dwpt_sample [C] Vaisala DMT242 			%.1f

Room/system temperature 			T_room [C] 	LM-35 temp sensor		%.1f

The first line in every file is a header line containing comma separated short names enclosed in double quotation marks. Data starts from line 2. The amount of uncompressed ASCII data is ca. 200 kB/day.