Second Wind sensor information and data format.

Levels 50, 100, 150, and 200m are instrumented with Second Wind cups and wind vanes. There are cups on both sides of the tower (334o and 154o). Wind vanes are on the south booms. Most data are 10 min averages.

Sept 2008 has 10 min and 1 min wind speeds for part of the time

Aug 2009 has 10 min and 1 min wind speeds for part of the time

The sensors are:

Anemometers Model:SWI C3C

http://www.secondwind.com/Products+Systems/Nomad/NomadProducts/pn981.html

Wind Vane Model:SWI PV1

http://www.secondwind.com/Products+Systems/Nomad/WindVanesList.shtml

Temperature Model:SWI 10k Probe (Non aspirated radiation shields)

http://www.secondwind.com/Products+Systems/Nomad/TempSensorsList.shtml

Data are collected via a Nomad2 data logger

InputID

Input

Logger			Data logger number

Stationheight		Height of sensor (m)

Stationazimuth		Boom angle (True)

funcnctionOf		Parameter measured

functionInterval 	Averaging period (sec)

FunctionName 		type of value (average, Std Dev, Max Value, Vec Average)

Timestamp		seconds since 1996/1/1 (beginning or averaging period)

This is the MATLAB code to convert the time stamp value into date time:

y(i) = T/(60*60*24);  % Number of days since 01/01/1996 00:00:00

z(i) = y(i)+ datenum([1996,1,1,0,0,0]);

dt = datestr(z(i), 31);    % convert serial days to date string

The datenum function converts date vectors into serial date numbers. Date numbers are serial days elapsed from some reference date. By default, the serial day 1 corresponds to 1-Jan-0000.

datavalues

speed (m/s)

direction (degrees True)

temperature (degrees C)

MATLAB programs written by Dan Wolfe to read Second Wind data

read_2nd_wnd.m

MATLAB program written to read BAO data

Bao10100300_