Summery AMMA 2008 (African Monsoon Multidisciplinary Analysis)

This summery will sum up observations, problems, etc during the AMMA cruise in 2008.

The cruise was going from Montevideo, Uruguay to Charleston, South Carolina from April 27th to May 18th.

Also some data analysis results will be shown here, especially an overview on the calibrations will be given so that these and other important information will be available for people working on the cruise data but didn’t participate.

Instructions: For additional information on the instrumentation and instructions how to run the instrument read ‘San Diego’, ‘Directions for operating the Fast Ozone Sensor.doc’, and Diploma thesis ‘Ozone flux measurements during the Gulf of Mexico and East Coast Carbon Cruise 2007 (GOMECC)’.

- Where to find the data at NOAA

Data for the AMMA cruise can be found at ‘R:\AMMA_2008\KathrinsData’. The raw data can be found in R:\AMMA_2008\RHB\flux\Raw

Comments on subfolders:

- ‘AMMA_calibrations_etc’	calibrations, overviews from cruise, several instrument issues, etc.

- ‘AMMA_DEC08’	read ‘Comments_AMMA_DEC08.txt’

- ‘AMMA_NOV08’	read ‘Notes_AMMA_NOV.txt’

- ‘AMMA_SEP08_final_paper’	Final Data, including smoothing correction, data for 
		paper; read ‘Note on AMMA_SEP08.txt’

- ‘MATLAB_general’		matlab files for corrections such as smoothing correction

- Parameters and Acronyms

Instrument Parameters and Acronyms

Set point

PLF 		purge line flow			12 lpm

SF		sample flow				1.25 lpm

NOf		nitric oxide flow			3 mlpm

O3f		uv ozone monitor			0.5 lpm

Nafionf	Nafion flow				2.5 lpm

PLP		purge line pressure			~

NFP		Nafion pressure			~

PMT		Photomultiplier tube			-17 to -17.7 degC

RCT		Reaction Chamber Temperature	25 degC

RCP		Reaction chamber Pressure		P = 18 Torr

HV		High Voltage				1500 V

Purge Line length					118ft

General Acronyms

DOY		Day of year

- Cruise Description

Below observations and events for this experiment are listed by day of year in 2008 and GMT time.

Day 119	16:00-18:00, insert zero air

16:00-20:00, insert 20 ppb O3 (peak issue investigations)

Day 120	11:00-13:00, calibration from box

14:00-16:00, insert 20 ppb O3

16:00-20:00, insert zero air

Day 121	12:00-?, insert O3, NO flow controlled with needle valve

Day 122	count drop

Sample flow down

Day 123	10:30 (pm?), count drop back

Day 125	10:00, shut down instrument to fix loose wire

20:00, shut down instrument over night since flows are not working

Day 126	system repair day

17:00, instrument back on

18:00, flows back to normal

Day 127	SF and AF dead, exchange MFC’s

Day 128	running a few tests! Check MFC flows and this day!

Day 129	10:00:12:00, calibration from mast

12:00-13:00, insert high ozone for 1 hr

16:00-18:00, calibration from mast

18:30-20:30, calibration from box

Day 131	17:00, few short tests,

Day 133	12:20, check for test performed

19:00, calibration from box

Day 135	16:00, insert different concentrations into system with and without Nafion

Day 135, 	14:00, calibration from box

Day 138	14:00, calibration from box

- Calibrations

Calibrations were performed 12 times. Some day several were performed, from the mast or the box and table 1 is then showing the average (see also Instructions).

There are two options how to calculate the ozone mixing ratio in ppb from the calibrations. One option is to average the calibration functions. The average of the slope is then 2735.69 counts s-1, for the y-intercept it would be 3933.18 counts s-1. Therefore ozone in ppb would be

Table 1: Calibrations

| Julian Day | slope | y-intercept |
| --- | --- | --- |
| 106.00 | 3025.849 | 3809.182 |
| 108.00 | 2632.083 | 5528.315 |
| 116.00 | 2982.53 | 6244.55 |
| 120.00 | 2941.393 | 5186.441 |
| 129.00 | 2698.57 | 2797.114 |
| 133.00 | 2501.789 | 613.9283 |
| 136.00 | 2548.102 | 3439.337 |
| 139.00 | 2555.228 | 3846.605 |
| mean | 2735.692 | 3933.183 |
| stdev | 214.4799 | 1774.114 |

Figure 2.2: all calibrations during AMMA cruise. Those that do not say ‘mast’ were done from the box.

Second, slopes and y-intercept can be plotted and the resulting functions can be used for calculating O3 in ppb (Figure 2.1).

The result for AMMA 08 would be:

Figure 2.1: slope and y-intercept of the calibrations

- Lag-time

The lag-time is described in the instruction files. On AMMA, no lag-time tests were performed since there were problems to fill the gas reservoir. During AMMA the instrument was running the exact same way than during GASEX which was the cruise right before. There, lag-time test were performed daily. The result was 5.4 s which is thus used in the data analysis for AMMA.

- Figures

4.1 Concentrations along the ship track

To plot the mixing ratio or the flux along the ship track:

First use ‘map’ until delx=.25;

Then apply following:

CLIP  = 'on';

[x,y] = m_ll2xy(lon,lat,'clip',CLIP); colormap;

hold on ; scatter(x, y, 25, H)

H is the variable you want to plot. Usually you also want to apply a filter, thus you have to write x(p), … p is the filter, the data you want.

4.2 Wind direction along the ship track

To plot the wind direction you need the wind vectors U and V from the ‘da-file’, U or Ue is column 40 and V or Un column 39.  First make 1 hour averages. Then do following:

use ‘map’ until delx=.25;	Then apply from ‘m_track’ file:

CLIP  = 'on';

[x,y] = m_ll2xy(lon,lat,'clip',CLIP); colormap;

hold on ; quiver(x, y, Ue, Un, 25)

- Filters

- Wind speed < 0.5 m*s-1

ii=find(u<0.5);

- Relative wind direction

ii=find(reldir<270 & reldir>90);

- Rain

ii=find(rain>5);

- Ozone mixing ratio below 5ppb or above 80 ppb since these values are usually not observed

ii=find(O3ppb<5 | O3ppb>100);

- Ozone standard deviation

ii=find(O3std>3 | O3std<-3);

- Delta Ozone; difference between 2 10min mean values. Is difference too big it indicates an unusual drop/increase

ii=find(deltaO3>3 | deltaO3<-3);

- motion correction

ii=find(sp2>2);

- Ship speed, indicates maneuver

ii=find(sig_u> 0.5);

- Standard deviation heading, indicates ship maneuver

ii=find(sig_h> 8);

- Filter developed by hand for calibration, wrong flow rates, missing data,…

ii=find(isnan(hand));

All filters are combined in the text-file ‘AMMA_filter_final’. The columns are:

jd=data(:,1);               %julianday

sp=data(:,2);               %ship speed

u=data(:,3);                %wind speed

reldir=data(:,4);           %relative wind direction

rain=data(:,5);             %NaN=rain>5

lag=data(:,6);              %lagtime

O3ppb_o=data(:,7);          %O3ppb

deltaO3_o=data(:,8);        %delta between 2 consecutive O3 values

O3std_o=data(:,9);          %standard deviation

O3ppb=data(:,10);           %O3ppb

deltaO3=data(:,11);         %delta between 2 consecutive O3 values

O3std=data(:,12);           %standard deviation

sp2=data(:,13);             %motion correction

sig_u=data(:,14);           %std dev of ship speed, m/s

sig_h=data(:,15);           %std dev of heading

hand=data(:,16);            %missing data, calibrations, flows,…

total_o=data(:,17);         %total filter crosscorr without lag

total=data(:,18);           %total filter constant lagtime without lag

‘_o’ indicates that this data is from cross correlation, equivalent other data is of constant lag-time method