## Slide 1
23 Nov 2019: flux measurements – ‘dark side’ : two locations, 1 over 140 cm deep ice, 2 over 15 cm new ice.
There’s a slight difference in flow rate when the instrument is in chamber mode. Why?
Equals about 0.01 SLPM difference
Ambient concentrations
Methane analyser:
CH4air: 1964.346 ppb
CH4sd: 0.1113127
CO2 418.3644
CO2sd 0.5725538
H2O 970.0163
H2Osd 15.58204

## Slide 2
23/11/19: Site 1 (deep ice -10 cm snow): CO2
Two Sample t-test
p-value = 2.246e-07
alternative hypothesis: true difference in means is not equal to 0
95 percent confidence interval:
-0.015604240 -0.007060385
mean of x mean of y
-0.01033 0.000995
Flux/day (deposition ?) ug/m2/d: -705.8
umol/m2/d: -16.04

## Slide 3
23/11/19: Site 1 (deep ice -10 cm snow):
CH4
Flux/day (deposition) ng/m2/d: -1511.153
nmol/m2/d: -94.44703
Two Sample t-test:data:
mean of x mean of y
-0.0515725091 0.0007844477
p-value = 1
alternative hypothesis: true difference in means is greater than 0
p-value < 2.2e-16
alternative hypothesis: true difference in means is not equal to 0
p-value < 2.2e-16
alternative hypothesis: true difference in means is less than 0

## Slide 4
23/11/19: Site 1 (deep ice -10 cm snow): CH4
Reduced Start (inlet) sequence – may be more reliable to use in this case.
Should also consider using only samples after 4tau – i.e. 1200 s – will still show a depoisition

## Slide 5
23/11/19: Site 2 (new ice -10 cm): CO2
Two Sample t-test: t = -8.5539, df = 1004, p-value < 2.2e-16
alternative hypothesis: true difference in means is not equal to 0
95 percent confidence interval:
-0.02484735 -0.01557434
sample estimates: mean of x mean of y
-0.0200740232 0.0001368198
variables Obs
1 Date 23Nov19 > 3875 sec
Location Site 2 Gas CO2
Flux/day (ug/m2) -1263.0999 Flux/day (umol/m2) -28.7068 Q1 (SLPM) 7.596

## Slide 6
23/11/19: Site 2 (new ice -10 cm): CH4
Two Sample t-test
data: Cavg and Iavgt = 11.776, df = 1567, p-value < 2.2e-16
alternative hypothesis: true difference in means is not equal to 0
95 percent confidence interval: 0.04762250 0.06665766
sample estimates: mean of x mean of y
0.0575226251 0.0003825445
Flux / day:
ug/m2/d: 1298.558
nmol/m2/d: 81.160