Nauru99 Cruise Radiometer Report

Hughs

August 30, 2006

Duane Hazen

Summary

The Microwave Radiometer from the Hughs radiometer data has been reprocessed.  The tip curve calibration hand calculated from all the tip curves taken.  The main point used for good or bad was symmetry of the tip curve, the next was the air mass error.

The Radiometer and Sond vapor and liquid for the cruise looked like this.

NOTE:  The data is presented in units of cm for vapor and g/m2 for liquid.  The spikes in liquid indicate major rain events

Scatter plots of sond verses radiometer look like this.

NOTE: That the sond data used was the original sonds with no corrections.

QC plot of TB23 verses TB31

The mean difference numbers are. (Sond – Mailbox)

| Variable | Mean Difference |
| --- | --- |
| TB 23.8 GHz | -11.336873 |
| TB 31.6 GHz | -7.419747 |
| Vapor | -1.125696 |
| Liquid | -67.618091 |