PACS 2001 Cruise Radiometer Report

Model 1100

July 6, 2006

Duane Hazen

Summary

The Microwave Radiometer Model 1100 data has been reprocessed.  The tip curve calibration acceptance test was adjusted to account for weather and sea conditions to keep the radiometer in calibration.  NOTE: The raw tipcurve information was not in the data files so the processed tips in the .tip files was used in place of recalculating tip curves each time.

The Radiometer and Sond vapor and liquid for the cruise looked like this.

NOTE:  The data is presented in units of cm for vapor and g/m2 for liquid.  The spikes in liquid indicate major rain events

Scatter plots of sond verses radiometer look like this.

QC plot of TB23 verses TB31

The mean difference numbers are. (Sond – Mailbox)

| Variable | Mean Difference |
| --- | --- |
| TB 23.8 GHz | -0.619920 |
| TB 31.6 GHz | 0.619674 |
| Vapor | -0.207675 |
| Liquid | -47.459355 |