20180915
Morning Shift (9A-1P L)
Ben Tabing

0000 – Scanning strategy set to one volume scan with intermittent surveillance scans per hour to reduce the stress on the radar since no convection is in range.

0200 – A volume scan shows no precipitation features found in the radar observing area.

Afternoon Shift (1P-9P LT)
Weixin Xu

0400 — Stay in the scan mode with mix of one volume scan PISTON_FAR_S (8 angles from 0.8 t0 6.7) and 3 surveillance scans (one angle at 0.8) hourly. Some precipitation echoes appear in the far northeast over 150 km from the radar.

0555 — Switch to the FAR volume scan mode (24 tilts), as some isolated convective cells move into the 100 km radar domain from the north. FAR volume scan is conducted once every hour, with additional three surveillance scans. The estimated echo top is around 6 km (echoes at 100 km seen at 3.7 degree elevation angle).

0655 — Return to the mode of volume scan plus surveillance scan.

0755 — Change the scan strategy to PISTON_FAR (24 angles from 0.8 to 21.2) every 15 min to check out the scattered convection to the west of the radar. These convective cells are just shallow rain showers with tops just close to the freezing level (5 km).

0830 — Switch to PISTON_Low scan mode (24 angles from 0.8 to 16.9) and scan every 15 min to sample the shallow warm rain showers (maximum echoes of 45 dBZ).

1000 — Return to the scan strategy with one volume scan (PISTON_FAR_S) followed by three surveillance scan every hour.

Night Shift (9P – 5A LT)
Chelsea Nam

1150 – As surveillance scan shows some convective cells at the northeast domain, PISTON_FAR_S was conducted. Echo top ~8 km, maximum reflectivity ~45 dbz at 100km range.

1204 – Surveillance scan shows the convection northeast between 100-200km, but the ~120 km range scan can’t capture the system well.

1255 – Switched to PISTON_FAR to catch the convective cell as it was inside 120 km range domain. The systems looks to be an area of disorganized convection around 14N 136E from IR Himawari-8 imagery at 0915 1210 UTC (see below figures). Echo top locates ~6.5 km.

1320 – Change to PISTON_LOW for the system currently in the radar domain is shallow.

1409 – Tried RHI_S with 65 km range and 30-90 azimuths – nothing special, so came back to PPI mode (PISTON_LOW)

1552 – We are having a light rain outside. As the ship moves to the north the convection is now mainly to the south of the radar where the radar is blocked. On the next round, the scan will be changed to surveillance to see if there are other convective systems far and to save the radar from wearing.

1602 – From surveillance scan, some convection is found at northeast domain between 150 – 300 km. Still far.

1800 – Volume scan (FAR_S) is going on and it shows isolated convection NWN at ~40km range echo top > 6km

1805 – Another volume scan (FAR) is conducted to resolve the echo top (~9 km).

1820 – Surveillance mode again.

1850 – Scattered convection over the domain but mostly northeast ranged 100-300 km.

Morning Shift
Ben Trabing (5A-9A L)

2000 – Conducted full volume scan with 24 angles. Isolated convective cells are located between 245-270 degrees and 110-135 degrees with an area of stratiform precipitation towards the north-northwest (15-45 degrees). Convection is relatively shallow.

2030 – Himiwari-8 10.4 IR shows predominant warming of brightness temperatures (lag ~30 minutes) while several areas around radar have transitioned to broad lower reflectivities associated with stratiform precipitation

2200 – Continue far volume scans and intermittent surveillance scans. There remains shallow stratiform precipitation towards the north of the ship.