20180925
Morning Shift (9A-1P L)
Ben Trabing

0000 – Radar was down and required maintenance.

RADAR IS DOWN UNTIL FURTHER NOTICE

Afternoon Shift (11A-9PL)
Weixin Xu

0200 – Problem fixed and radar resume operation. First tested in the SURVEILLANCE scan, and then the FAR-S scans, both looking good.

0215 – Switch to FAR PPI scans. Some scattered convection appears in the 100 km radar domain.

0415 – Run a SURVEILLANCE to check out convection further from the radar, as there is only a few tiny convective cells in 100 km range.

0415 – Radar is operated in running SURVEILLANCE and FAR_S scans, as convection is calm.

0800 – Change to FAR PPI mode to observe some larger convective features approaching the radar from 80-100km northeast.

Night Shift (9P-4A L)
Chelsea Nam

1200 – FAR PPI mode, linear convective system in northwest in 75 – 120 km range with shallow warm rain cells having high Z & Zdr.

1210 – Interesting feature about the convective system evolution from 1145 scan comparing to 1130 scan. The linear high Zdr core shown in the previous scan is now diminishing, but new line of convection has appeared west to the existing line with high reflectivity and Zdr. Wonder if it’s from cold pool effect.

1219 – There is a clear convergence line in the convective system from 1200 scan.

1245 – Change into LOW from 1245 scan to have better resolution below 16.9 deg tilt - no reflectivity appears above 7 deg in the domain.

1305 – 1245 scan shows high dbz and zdr cell in the linear system again. It is moving eastward as we have westerly from surface to 300 hPa according to the latest sounding.

1420 – This convective system is still producing high zdr high z warm rain cells in it - Zdr maximum ~5 dB, Z maximum ~55dBZ

1430 – The southern tip of the linear system still has very high Zdr (max ~5 dB) and Z core (max ~65 dBZ).

1445 – 1430 scan shows the cho top is now reaching almost 16 km with ice particles and negative Zdr.

1530 – The ship rotated and now the convective system northeastnorth to the radar is blocked by the bridge.

1600 – A few isolated shallow convection in the domain (still LOW volume scan mode)

1630 – Convective cells are moving to the northeast.

1700 – Two new cells popped up in the west side with very high reflectivity and Zdr.

1730 – Small warm rain convection is still in the west domain. Several cells decayed but several newly popped up.

1830 – Still having several shallow big drop-sized warm rain cells in the domain – keeping the LOW volume scan.

Morning Shift (4A-9A L)
Ben Trabing

1900 – Continue high number of low elevation angles to resolve few cells ~ 100 km away to the northwest.

1930 – Spatial coverage of shallow convection has increased over the last scan partially due to cells moving into the area from the blocked region.

2145 – Shallow convection has mostly dissipated. Switch to surveillance scans and Far_S. The ship has rotated with a heading towards 30. This means that upstream convection will not be sampled until the ship turns or the convection moves downstream.

2310 – No convection is found in the radar domain.