## Slide 1: Utility of shipborne disdrometer and marine navigation radar observations during convective and stratiform rain
CHRISTIAN KLEPP
Univ. of Hamburg
ELIZABETH J. THOMPSON, KYLA DRUSHKA, WILLIAM E. ASHER
Applied Physics Lab at Univ. of Washington

## Slide 2
SMAP
SSS
30-40
psu
IMERG
Rain
0-160
mm h-1
Surface Salinity or soil moisture
Rain
E. J. Thompson AMS Radar 2017
Interest in precipitation impacts on ocean renewed because of:
global climate projections, SST impacts, and satellite salinity measurements
NASA SMAP L-band radiometer: 40 km, 9 day resolution
April – July 2015 NASA Hyperwall: https://svs.gsfc.nasa.gov/30698
Notes: Soil Moisture, Sea Surface Salinity, and Rainfall
This visualization compares weekly soil moisture and sea surface salinity data (over land and water, respectively) from NASA’s Soil Moisture Active Passive Satellite (SMAP) mission [<i>top map</i>] with a precipitation product called Integrated Multi-satellite Retrievals for GPM, or IMERG [<i>bottom map</i>], from April 17 to August 2, 2015. IMERG is derived using data from the Global Precipitation Measurement (GPM) international constellation of satellites.
These maps reveal how precipitation amounts influence soil moisture conditions and sea surface salinity. For example, high amounts of precipitation along the equator coincide with relatively moist soil conditions on land (blue shades) and low salinity values in the ocean (green and blue shades). Conversely, areas that receive little or no precipitation, such as the Sahara Desert in northern Africa, coincide with dry soils (dark yellow shades). Scientists can use data from SMAP and IMERG to develop improved flood prediction and drought monitoring capabilities. Societal benefits include improved water-resource management, agricultural productivity, and wildfire and landslide predictions. Data from SMAP also allow us to extend the data record of the highly successful 3-year Aquarius sea surface salinity mission into the future.
For more information, visit:
svs.gsfc.nasa.gov/goto?30698

## Slide 3: Radars and disdrometers are needed to better understand several coupled climate and weather processes over oceans
Need ways to contextualize ship point measurements to synoptic and satellite-observable scales
Upstream rainfall is important for understanding local salinity and temperature structure in the ocean, but to an unknown degree.
Drop size impacts ocean turbulent mixing, which is parameterized in ocean models
E. J. Thompson AMS Radar 2017
?
?
?
?
?
?
?
?
?
?
?
?
Local
Data
Advected freshwater by ocean current
Notes: Representativeness problem:
Research ships struggle with “representativeness” problem
research ship is just one point in the ocean
research ship is actually in the cone of silence
disdrometer in center of radar might actually be a way to bridge that gap; gauge can do quantitative work but disdrometer can explain morphology
Similarly over land, disdrometers and aircraft probes help verify physics we think we see in radar variables. It’s symbiotic because radars also help remotely broaden the field of view compared to several gauges or disdrometers.
We think upstream precipitation matters for underlying ocean variability; radars can help.
We always need a way to justify high costs of ship measurements and a way to connect them to larger scales of satellites - a ship board disdrometer can help describe larger scale features or place us within the large scale feature that might actually be visible from satellite scale. This could be a really great tool. It’s compact too - easy to delpoy on a ship.
Develop the capability for shipborne disdrometers and radars to quantify spatial and temporal variability of local and upstream rainfall, which will help contextualize local atmospheric and ocean measurements, and connect them to the satellite-scale… so that we can learn how to remotely quantify these sub grid scale processes.
Supports ground validation of satellite rain retrievals over ocean, which are usually underestimated or missed due to partial beam filling, prevalence of shallow warm rain processes, and lack of gauges.
Convective vs. stratiform hypotheses
Upstream rainfall must be quantified to understand in situ ocean processes
While intense convective rainfall has been hypothesized to impact the ocean mixed layer depth more, stratiform rain possesses a longer and larger window of opportunity to alter ocean physics.
Because these processes have not yet been measured until recently, It is still unknown how the spatial and temporal variability of rain impacts ocean variability.
SSS will be assimilated into global models… need to understand the physics associated with rain impacts on the ocean surface.

## Slide 4: Radars and disdrometers are needed to better understand several coupled climate and weather processes over oceans
Need ways to contextualize ship point measurements to synoptic and satellite-observable scales
Upstream rainfall is important for understanding ocean salinity and temperature structure, but to an unknown degree.
Drop size impacts ocean turbulent mixing, which is parameterized in ocean models
Central Indian Ocean Shipborne Radar
Zh
E. J. Thompson AMS Radar 2017
?
?
?
?
?
?
?
?
?
?
?
?
Local
Data
Advected freshwater by ocean current
Notes: Representativeness problem:
Research ships struggle with “representativeness” problem
research ship is just one point in the ocean
research ship is actually in the cone of silence
disdrometer in center of radar might actually be a way to bridge that gap; gauge can do quantitative work but disdrometer can explain morphology
Similarly over land, disdrometers and aircraft probes help verify physics we think we see in radar variables. It’s symbiotic because radars also help remotely broaden the field of view compared to several gauges or disdrometers.
We think upstream precipitation matters for underlying ocean variability; radars can help.
We always need a way to justify high costs of ship measurements and a way to connect them to larger scales of satellites - a ship board disdrometer can help describe larger scale features or place us within the large scale feature that might actually be visible from satellite scale. This could be a really great tool. It’s compact too - easy to delpoy on a ship.
Develop the capability for shipborne disdrometers and radars to quantify spatial and temporal variability of local and upstream rainfall, which will help contextualize local atmospheric and ocean measurements, and connect them to the satellite-scale… so that we can learn how to remotely quantify these sub grid scale processes.
Supports ground validation of satellite rain retrievals over ocean, which are usually underestimated or missed due to partial beam filling, prevalence of shallow warm rain processes, and lack of gauges.
Convective vs. stratiform hypotheses
Upstream rainfall must be quantified to understand in situ ocean processes
While intense convective rainfall has been hypothesized to impact the ocean mixed layer depth more, stratiform rain possesses a longer and larger window of opportunity to alter ocean physics.
Because these processes have not yet been measured until recently, It is still unknown how the spatial and temporal variability of rain impacts ocean variability.
SSS will be assimilated into global models… need to understand the physics associated with rain impacts on the ocean surface.

## Slide 5: Radars and disdrometers are needed to better understand several coupled climate and weather processes over oceans
Need ways to contextualize ship point measurements to synoptic and satellite-observable scales
Upstream rainfall is important for understanding ocean salinity and temperature structure, but to an unknown degree.
Drop size distributions provide clues about surrounding rain variability
Central Indian Ocean Shipborne Radar
Zh
E. J. Thompson AMS Radar 2017
?
?
?
?
?
?
?
?
?
?
?
?
Local
Data
Advected freshwater by ocean current
Notes: Representativeness problem:
Research ships struggle with “representativeness” problem
research ship is just one point in the ocean
research ship is actually in the cone of silence
disdrometer in center of radar might actually be a way to bridge that gap; gauge can do quantitative work but disdrometer can explain morphology
Similarly over land, disdrometers and aircraft probes help verify physics we think we see in radar variables. It’s symbiotic because radars also help remotely broaden the field of view compared to several gauges or disdrometers.
We think upstream precipitation matters for underlying ocean variability; radars can help.
We always need a way to justify high costs of ship measurements and a way to connect them to larger scales of satellites - a ship board disdrometer can help describe larger scale features or place us within the large scale feature that might actually be visible from satellite scale. This could be a really great tool. It’s compact too - easy to delpoy on a ship.
Develop the capability for shipborne disdrometers and radars to quantify spatial and temporal variability of local and upstream rainfall, which will help contextualize local atmospheric and ocean measurements, and connect them to the satellite-scale… so that we can learn how to remotely quantify these sub grid scale processes.
Supports ground validation of satellite rain retrievals over ocean, which are usually underestimated or missed due to partial beam filling, prevalence of shallow warm rain processes, and lack of gauges.
Convective vs. stratiform hypotheses
Upstream rainfall must be quantified to understand in situ ocean processes
While intense convective rainfall has been hypothesized to impact the ocean mixed layer depth more, stratiform rain possesses a longer and larger window of opportunity to alter ocean physics.
Because these processes have not yet been measured until recently, It is still unknown how the spatial and temporal variability of rain impacts ocean variability.
SSS will be assimilated into global models… need to understand the physics associated with rain impacts on the ocean surface.

## Slide 6: Motivation
Understand the capabilities of a shipborne optical disdrometer and X-band marine navigation radar for sensing stratiform and convective rain
Marine navigation radars are different than weather radars, but are standard equipment on research vessels
OceanRAIN project has deployed ODM470 optical disdrometers on several long term cruises (Klepp 2015, Atm. Res.)
E. J. Thompson AMS Radar 2017
Optical Disdrometer
Attached to anemometer;
rotates into wind to minimize flow distortion

## Slide 7: X-band Marine Navigation Radar
7 hours of tropical E. Pacific rain
  3 stable freshwater lenses
3 updates per minute
1º horizontal beam width
Rain gauge indicated rain when echoes were overhead
Adjustable signal gain ~ “relative reflectivity” output
48 km range
E. J. Thompson AMS Radar 2017

## Slide 8: Marine radar qualitatively revealed stratiform and convective rain morphology on 1-min time scales
Could use data to motivate intensive field campaigns with research quality radar
48 km range = 25 IMERG pixels… plenty of satellite validation opportunities
48 km range = 2.5-6 hr ship steaming; 15 hr advective time scale
Isolated convection
Stratiform
Stratiform with embedded convection
48 km range
Organized Convection
E. J. Thompson AMS Radar 2017

## Slide 9: Marine Radar Problem: 20º vertical beam width
Designed to see targets on sea surface regardless of sea state
Cannot distinguish: Rain aloft or rain at surface?
Tropical 0ºC Layer
Beam is 6 km tall at
40 km range
Beam hits melting layer at 25 km range
E. J. Thompson AMS Radar 2017

## Slide 10: Marine Radar Problem: Attenuation and artificial (?) echo brightening ~8 km range ~2 km high
48 km range
E. J. Thompson AMS Radar 2017
Notes: Maybe its okay for stratiform rain to attenuate… we know its more homogeneous. But we would miss embedded convection

## Slide 11: ODM disdrometer performance at sea
Sea spray not a terrible problem if mounted high enough (20 m)
Small log-scale size bins
Flow distortion minimized but fall speed still parameterized
Ship vibrations prevent drop detection below 0.43 mm
Lempio et al. (2007 Adv. Geosci.);
Klepp et al. (2010 Tellus);
Klepp (2015 Atm. Res.)
E. J. Thompson AMS Radar 2017

## Slide 12: Shipboard disdrometer: produces DSD parameters, …but 0.43 mm drop diameter detection limit complicates convection vs. stratiform separation. Solution: use rain duration
E. Pacific DSD: ODM 470
W. Pacific DSD: 2DVD
W. Pacific DSD: 2DVD
E. J. Thompson
AMS Radar 2017
?
Should conduct more side-by-side disdrometer tests on land
Thompson et al.
2015 JAS
Convective
Stratiform

## Slide 13: Summary: shipborne marine radar and disdrometer
X-band Furuno marine navigation radar:
  Very high spatial and temporal resolution; very qualitative
  Great resource for detecting spatial patterns and relative intensity of rain
ODM 470 optical disdrometer:
  Fine bin size resolution; sea spray not a problem in most cases
  Future: minimize ship vibration impact
  Future: need side-by-side comparison
2010-2014 ship disdrometer opportunities, including North Pole crossing
E. J. Thompson AMS Radar 2017

## Slide 14
Impacts:
  Ocean turbulence
  SST --> Rain
  Hydrologic and energy budgets
E. J. Thompson AMS Radar 2017
Miller et al. 1976, Anderson et al. 1996, Soloviev and Lukas 2006, Drushka et al, 2014a,b, 2016, Asher et al. 2014, Boutin et al. 2014, Thompson et al. in prep
Illustration c/o
Kyla Drushka
Salt water
Fresh water