STRATUS 2005 Cruise Radiometer Report

Hughs

September 15, 2006

Duane Hazen

Summary

The Microwave Radiometer from the Hughs radiometer data has been reprocessed.  The tip curve calibration hand calculated from all the tip curves taken.  The main point used for good or bad was symmetry of the tip curve, the next was the air mass error.

NOTE:  The liquid and vapor was found from a three channel retrieval if the 90 GHs brightness temperature was greater than 2.75 K and less than total mean radiating temperature.

The Radiometer and Sond vapor and liquid for the cruise looked like this.

NOTE:  The data is presented in units of cm for vapor and g/m2 for liquid.  The spikes in liquid indicate major rain events

NOTE: The data gap from mid day 290 to mid day 292 is from the 31.65 GHz Hot Load Temperature jumping 70 degrees C.  There are no tipcurves during this time to calibrate this time period with.

Scatter plot of sond verses radiometer look like this.

QC plot of TB23 verses TB31

The Brightness temperature looked like this.

The mean difference numbers are. (Sond – Mailbox)

| Variable | Mean Difference |
| --- | --- |
| TB 20.6 GHz | 2.875 |
| TB 31.6 GHz | 5.119 |
| TB 90.0 GHz | 26.575 |
| Vapor | 0.029 |
| Liquid | 127.388 |