VOCALS 2008 Radiosonde Log

| Date-Time (UTC) | # | Max mb | Max ht | Comment | GTS |
| --- | --- | --- | --- | --- | --- |
|  | T |  |  |  | X |
| 10/15/2008 11:33 | 1 |  |  | Old Sonde | X |
| 10/15/2008 1735 | 2 |  |  | Old Sonde | X |

VOCALS 2008 Radiosonde Log

| Date-Time (UYC) | # | Max mb | Max ht | Comment |
| --- | --- | --- | --- | --- |

Launch Schedule

UTC		Ship Time		Launch Time (Ship)

00			21			2030

04			01			0030

08			05			0430

12			09			0830

16			13			1239

20			17			1630

- Check Helium prior to launch (turn on and a min of 500 lbs left in tank: switch tanks if lower)

- Make sure laptop is connected to the SPS220 (gray network cable in back)

- Some of the balloon ties don’t stay tight (take extras and double check they are snug before releasing balloon)

- Once sonde is outside, compare readings to ship SCS (PC to right of laptop) to be sure the sonde sensors are working P-T-RH

- Check wind direction to determine where on stern to release balloon

- Call bridge (126) ~10 min prior to launch and ask to slow ship

After launch is finished:

- Turn off helium tank and note lbs  remaining in tank

- Close lid to ground check station

Send WMO messages to GTS

- Check for  4-temp(a,b,c,d).txt messages in D:\DigiCORAIII\messages\

- Switch out SPS220 cable with blue network cable

- Click on Sounding Data Manager GTS Icon

- Click on process button (note whether ftp was successful on log sheet)

Copy 4 latest files to folders on LaCie (ICON)

- D:\DigiCORAIII\data\ edt_WTEC*

- D:\DigiCORAIII\messages\ *_EDT_LATLON.txt

- D:\SoundingArchive    (*.dc3db)

- D:\WTEC\WMO\	(WTEC*.wmo)

Email LonLat files to catalog-vocals@eol.ucar.edu

Radiosonde Flight Log

Experiment:___VOCALS_2008

Location:______Ron Brown

Date/Time of Launch :_____________________(UTC)

Launch Crew:_________________________________________

Sonde type:  RS-92G    Ser No.______________________

Surface Obs fm SCS:

T (C):__________   RH (%):______________   Press (mb):_____________

WSpd (m/s)___________________   WDir (T):______________________

Use for SFC OBS in system

Surface Obs fm Sonde (acclimating on deck in shade):

T (C):__________  RH (%):______________ Press (mb):_____________

Local Satellites:_____________   Sonde satellites:_____________

Sonde Freq:_________________________

Helium (lbs):_________________________

Weather Obs:

Clouds:__________________    Cloud Cover:____________________

Precip:__________________

Comments:

Max Ht (m):______________   Min Press (mb):__________________

Reason for Termination:_____________________

FTP to GTS:                                                              ____________

gmail LatLon file                                                      ___________

catalog-vocals@eol.ucar.edu  Co.wolfegang   crwdew

Copy edt, wmo and dc2db files to H: DAS01        ____________

UTC              Ship Time                  Ship Time

Prep for launch                Balloon Release

00               2000                           2030

04               0000                           0030

08               0400                           0430

12               0800                           0830

16               1200                           1230

20               1600                           1630