Epic 2001 cruise on R/V Ronald H. Brown

C. Fairall and S. de Szoeke

2007 November 3

chris.fairall@.noaa.gov

The PSD radar group operated a microwave radiometer (MWR) manufactured by Radiometrics Inc. (Boulder) for this cruise.  Contact Duane Hazen (PSD) for details on the instrument.

Duane uses sondes and tipping calibrations to 're-calibrate' the results from the radiometer, but the data distributed at the end of the Stratus 2007 cruise has not been reprocessed and calibrated by Duane. From comparison with water vapor path from radiosondes released on the Stratus 2007 cruise, we have confidence in the microwave water vapor path retrievals. The liquid water path retrieval is more sensitive to calibration, so we have little confidence in it.

A MATLAB program is used to read hourly .raw files, strip out selected information, and write new files with the raw 21-s time resolution (STRATUS_2007_micro_s_f.txt). The data in this file is formatted in columns as follows:

STRATUS_2007_micro_s_f.txt

:,1  decimal julian date

:,2  IWV, integrated atmospheric water vapor (column precipitable water), cm

:,3  IWL, integrated cloud liquid content, cm

:,4  tau 20, optical thickness at 23 GHZ

:,5  tb 20, brightness temperature at 23 GHZ

:,6  tau 30, optical thickness at 31 GHZ

:,7  tb 30, brightness temperature at 31 GHZ

:,8  mode, instrument mode 00 is fix angle pointing 10 is tip curve calibration

:,9  tilt angle, for tip cal

:,10 cf20, calibration coefficient 23 GHz

:,11 cf30, calibration coefficient 31 GHz

:,12 sky20, detector voltage 23 Ghz pointing

:,13 nsky20, detector voltage 31 Ghz pointing + noise diode

:,14 bb20, detector voltage 23 Ghz black body

:,15 nbb20, detector voltage 23 Ghz black body + noise diode

:,16 tbb20, temperature of black body (K)

:,17 sky30,  detector voltage 31 Ghz pointing

:,16 nsky30, detector voltage 31 Ghz pointing + noise diode

:,19 bb30, detector voltage 31 Ghz black body

:,20 nbb30, detector voltage 31 Ghz black body + noise diode

:,21 tbb30,  temperature of black body (K)

:,22 pitch, deg

:,23 roll, deg

Minute and hourly averages are compiled in a more compact 6-column form:

STRATUS_2007_micro_h_f.txt and STRATUS_2007_ mn_f.txt

:,1  decimal julian date

:,2  IWC, integrated median atmospheric water vapor (column precipitable water), cm

:,3  IWL, integrated median cloud liquid content, cm

:,4  number of 21-s values used in median

:,5  standard deviation of IWV, cm

:,6  standard deviation of IWL, cm