L.Bariteau

July 12, 2009

Readme for met summary files

The 1-min daily ASCII files proc_name_DDD.txt (name=’pc’, ‘rad’, ‘scs’, or ‘son’; DDD=yearday where 000 GMT January 1, 2009 =1.00) are the daily files written at 1min resolution.

Most quantities given are subject to future modification based on accounting for other sources of data and revised calibrations.

Details:

* DDD=yearday where 000 GMT January 1, 2008 =1.00

* name=’pc’ refers to slow mean data (T/RH, PIR/PSP, etc)

* name=’rads’ refers to all data related to PSP and PIR sensors

* name=’scs’ refers to ship data system

* name=’son’ refers to sonic measurement.

The data columns are not labeled so they can be directly acquired with a MATLAB ‘load’ statement.

The columns for files proc_pc are as follow:

jdy=x(:,1);            % Day-Of-Year at beginning of time average

pir=x(:,2);            % averaged downward IR flux between Eppley unit and K&Z unit (W/m^2)

psp=x(:,3);            % averaged downward solar flux between Eppley unit and K&Z unit (W/m^2)

Tc1=x(:,4);            % case temperature of PIR Eppley unit (C)

Td1=x(:,5); );         % dome temperature of PIR Eppley unit 1 (C)

Tsea=x(:,6             % sea snake temperature, ~0.10 m depth (C)

Tvais=x(:,7);          % air temperature(C) (z~14 m)

Rhvais=x(:,8);         % Relative Humidity (%)(z~14 m)

org=x(:,9);            % rainrate, STI optical rain gauge, uncorrected (mm/hr) (z~15 m)

org_carrier =x(:,10);  % rain gauge function (V)

aspir_on=x(:,11);      % backflow indicator for RH/T sensor (V).

press=x(:,12);         % atmospheric pressure (mb)

The columns for files proc_rads are as follow:

jdy=x(:,1); 	% Day-Of-Year at beginning of time average

pir1=x(:,2);  	% downward IR flux from Eppley unit (W/m^2)

pir2=x(:,3);  	% downward IR flux from K&Z unit (W/m^2)

psp1=x(:,4);  	% downward solar flux flux from Eppley unit (W/m^2)

psp2=x(:,5);  	% downward solar flux flux from K&Z unit (W/m^2)

Tc1=x(:,6);   	% case temperature of PIR Eppley unit (C)

Td1=x(:,7);   	% dome temperature of PIR Eppley unit (C)

Tkz=x(:,8);   	% temperature of PIR K&Z unit (C)

Tvais=x(:,9);	% air temperature(C) (z~14 m)

Rhvais=x(:,10);   % Relative Humidity (%)(z~14 m)

Tsea=x(:,11);     % sea snake temperature, ~0.10 m depth (C)

The columns for files proc_son are as follows:

jdy=x(:,1);     % Day-Of-Year at beginning of time average

U=x(:,2);       % Relative u wind component (+boward) , m/s

V=x(:,3);       % Relative v wind component (+portward) , m/s

W=x(:,4);       % Relative w wind component (+up) , m/s

Tsonic=x(:,5);  % sonic temperature, C

dir =x(:,6)     % Relative wind direction (from),clockwise rel ship's bow, deg

Note: Sonic height is ~ 17.4 m above the water line.