PSD

August, 2011

Readme for summary files

The 1-min daily ASCII files DYNAMO_2011_proc_name_1min.txt (name=’met’, ‘rad’, ‘licor’, ‘son’ or ‘gpsnav’; are the composite files for the entire project written at 1min resolution.

Most quantities given are subject to future modification based on accounting for other sources of data and revised calibrations.

Details:

* name=’met’ refers to slow mean data (T/RH, PIR/PSP, etc)

* name=’rad’ refers to all data related to PSP and PIR sensors

* name=’ licor’ refers to Licor sensor (CO2/H2O)

* name=‘son’ refers to sonic measurement on the bow tower

* name= ‘gpsnav’ refers to the PSD navigation data from GPS units.

The data columns are not labeled so they can be directly acquired with a MATLAB ‘load’ statement.

The columns for files DYNAMO_2011_proc_met_1min.txt are as follow:

jdy=x(:,1);            % Day-Of-Year at beginning of time average

pir=x(:,2);            % averaged downward IR flux between Eppley units

psp=x(:,3);            % averaged downward solar flux between Eppley units

Tc1=x(:,4);            % case temperature of PIR Eppley unit (C)

Td1=x(:,5); );         % dome temperature of PIR Eppley unit (C)

Tsea=x(:,6             % sea snake temperature (C)

Tvais=x(:,7);          % air temperature(C)

Rhvais=x(:,8);         % Relative Humidity (%)

org=x(:,9);            % rainrate, STI optical rain gauge, uncorrected (mm/hr)

org_carrier =x(:,10);  % rain gauge function (V)

aspir_on=x(:,11);      % backflow indicator for RH/T sensor (V).

press=x(:,12);         % atmospheric pressure (mb)

Tc3=x(:,13);           % case temperature of PIR Eppley unit on 2nd deck (C)

Td3=x(:,14); );        % dome temperature of PIR Eppley unit on 2nd deck (C)

The columns for files DYNAMO_2011_proc_rad_1min.txt are as follow:

jdy=x(:,1); 	% Day-Of-Year at beginning of time average

pir1=x(:,2);  	% downward IR flux from Eppley unit #1 (W/m^2)

pir2=x(:,3);  	% downward IR flux from K&Z unit #2 (W/m^2)

psp1=x(:,4);  	% downward solar flux from Eppley unit #1 (W/m^2)

psp2=x(:,5);  	% downward solar flux from K&Z unit #2 (W/m^2)

Tc1=x(:,6);   	% case temperature of PIR Eppley unit #1 (C)

Td1=x(:,7);   	% dome temperature of PIR Eppley unit #1 (C)

Tc2=x(:,8);   	% case temperature of PIR Eppley unit #2 (C)

Td2=x(:,9);   	% dome temperature of PIR Eppley unit #2 (C)

Tvais=x(:,10);	% air temperature(C)

Rhvais=x(:,11);   % Relative Humidity (%)

Tsea=x(:,12);     % sea snake temperature(C)

The columns for files DYNAMO_2011_proc_licor_1min.txt are as follow:

jdy=x(:,1); 	       % Day-Of-Year at beginning of time average

Licor_H2O=x(:,2);        % Specific humidity (g/kg)

Licor_CO2=x(:,3);        % Licor CO2 (umol/mol)

Licor_Tempi=x(:,4);      % Licor temperature (degC)

Licor_Pressi=x(:,5);     % Licor pressure (hPa)

Licor_agci=x(:,6);       % Livor AGC value (%)

The columns for files DYNAMO_2011_proc_son_1min.txt are as follows:

jdy=x(:,1);     % Day-Of-Year at beginning of time average

U=x(:,2);       % Relative u wind component (+boward) , m/s

V=x(:,3);       % Relative v wind component (+portward) , m/s

W=x(:,4);       % Relative w wind component (+up) , m/s

Tsonic=x(:,5);  % sonic temperature, C

dir =x(:,6)     % Relative wind direction (from),clockwise relative to ship's bow, deg

The columns for files DYNAMO_2011_proc_ gpsnav_1min.txt are as follow:

jdy=x(:,1); 	    % Day-Of-Year at beginning of time average

gpslat1i=x(:,2);      % decimal latitude, deg

gpslon1i=x(:,3);      % decimal longitude, deg

gpsspeedi=x(:,4);     % GPS SOG, m/s

gpsheadi=x(:,5);      % GPS COG, deg

headxi_pitch=x(:,6);  % Crescent GPS heading #1, deg

pitchxi_pitch=x(:,7); % Crescent GPS angle (pitch), deg

pitchxi_roll=x(:,8);  % Crescent GPS angle (roll), deg

headxi_roll=x(:,9);   % Crescent GPS heading #2, deg

A second set of programs reads the daily 1-min text files; time matches the various data sources, averages them to 5 or 30 minutes, computes fluxes, and writes new daily flux files. The 5-min and 30-min daily flux files have been combined and rewritten as a single file to form the file DYNAMO_2011_PSD_flux_5min_all.txt and DYNAMO_2011_PSD_flux_30min_all.txt.

The column assignment for those files is as follow:

jdy=x(:,1); 	%Day-Of-Year at beginning of time average

s1t1=x(:,2);      %psd bow true wind speed, m/s

dir1t1=x(:,3);    %psd bow true wind direction, deg

ts=x(:,4);        %psd seasnake T, C

ts_tsg=x(:,5);    %ship thermosalinograph T, C  bow (NaN is not available)

sal_tsg=x(:,6);   %ship thermosalinograph salinity, psu  bow (NaN is not available)

ta=x(:,7);        %psd air T, C

qs=x(:,8);        %psd air specific humidity at sea surface, g/kg

qa=x(:,9);        %psd air specific humidity, g/kg

psp=x(:,10);      %psd solar flux, w/m^2

pir=x(:,11);      %psd IR flux, w/m^2

org=x(:,12);      %psd optical raingage precip rate, mm/hr

sogm5=x(:,13);    %SOG from gps, m/s

cogm5=x(:,14);    %COG from gps, deg

relsp1=x(:,15);   %relative bow wind speed, m/s

reldir1=x(:,16);  %relative bow wind direction, deg

lat=x(:,17);      %decimal latitude, deg

lon=x(:,18);      %decimal longtude, deg

zt=x(:,19);       %Depth of SST sensor used in heat flux calc, m

sig_sp=x(:,20);   %standard deviation of ship speed, m/s

taub=x(:,21);     %wind stress, coare 3.0, N/m^2

hsb=x(:,22);      %sensible heat flux, coare 3.0, w/m^2

hlb=x(:,23);      %latent heat flux, coare 3.0, w/m^2

rf=x(:,24);       %rain heat flux, w/m^2

ta_im=x(:,25);    %IMET air t, C  from RTD (NaN if not available)

qa_im=x(:,26);    %IMET air specific humidity from RTD, g/kg (NaN if not available)

s_shp1=x(:,27);   %ship port true wind speed, m/s (NaN if not available)

dir_shp1=x(:,28); %IMET port true wind direction, deg (NaN if not available)

psp_im=x(:,29);   %IMET solar flux, w/m^2 (NaN if not available)

pir_im=x(:,30);   %IMET IR flux, w/m^2 (NaN if not available)

pressm=x(:,31);   %Barometric pressure, mb

rh_psd=x(:,32);   %RH (%)

Finally, below are reference heights (with respect to water line) of the sensors used in the DYNAMO2011 experiment.

| Sensor | Sampling rate | Height (m) |
| --- | --- | --- |
| Bow sonic | 10 Hz | ? |
| Motion Pack | 10 Hz | ? |
| ORG | 0.1Hz, averaged to 1 sample/min | ? |
| T/RH | 0.1Hz, averaged to 1 sample/min | ? |
| Licor7500 (CO2&H2O) | 10 Hz | ? |
| Radiometers (top PSD van) | 0.1Hz, averaged to 1 sample/min | ? |
| Barometer | 0.1Hz, averaged to 1 sample/min | ? |
| SST | 0.1Hz, averaged to 1 sample/min | -0.05 to -0.10 |

Table 1.1. PSD sensor heights and sampling rates.