L.Bariteau

June, 2012

Readme for summary files

The 1-min daily ASCII files WHOTS_2012_proc_name_1min.txt (name=’met’, ‘rad’, ‘licor’, ‘son’ or ‘gpsnav’; are written at 1min resolution. Most quantities given are subject to future modification based on accounting for other sources of data and revised calibrations.

Details:

* name=’met’ refers to slow mean data (T/RH, PIR/PSP, etc)

* name=’rad’ refers to all data related to PSP and PIR sensors

* name=’ licor’ refers to Licor sensor (CO2/H2O)

* name=‘son’ refers to sonic measurement on the bow tower

* name= ‘gpsnav’ refers to the PSD navigation data from GPS units.

The data columns are not labeled so they can be directly acquired with a MATLAB ‘load’ statement.

The columns for files WHOTS_2012_proc_met_1min.txt are as follow:

jdy=x(:,1);            % Day-Of-Year at beginning of time average

pir=x(:,2);            % averaged downward IR flux between Eppley units (W/m^2)

psp=x(:,3);            % averaged downward solar flux between Eppley units (W/m^2)

Tc1=x(:,4);            % case temperature of PIR Eppley unit on bridge (C)

Td1=x(:,5); );         % dome temperature of PIR Eppley unit on bridge (C)

Tsea=x(:,6             % sea snake temperature (C)

Tvais=x(:,7);          % air temperature(C)

Rhvais=x(:,8);         % Relative Humidity (%)

org=x(:,9);            % rainrate, STI optical rain gauge, uncorrected (mm/hr)

org_carrier =x(:,10);  % rain gauge function (V)

aspir_on=x(:,11);      % backflow indicator for RH/T sensor (V).

press=x(:,12);         % atmospheric pressure (mb)

The columns for files WHOTS_2012_proc_rad_1min.txt are as follow:

jdy=x(:,1); 	% Day-Of-Year at beginning of time average

pir1=x(:,2);  	% downward IR flux from Eppley unit 1 on bridge (W/m^2)

pir2=x(:,3);  	% downward IR flux from Eppley unit 2 on bridge (W/m^2)

psp1=x(:,4);  	% downward solar flux from Eppley unit 1 on bridge (W/m^2)

psp2=x(:,5);  	% downward solar flux from Eppley unit 2 on bridge (W/m^2)

Tc1=x(:,6);   	% case temperature of PIR Eppley unit 1 (C)

Td1=x(:,7);   	% dome temperature of PIR Eppley unit 1 (C)

Tc2=x(:,8);   	% case temperature of PIR Eppley unit 2 (C)

Td2=x(:,9);   	% dome temperature of PIR Eppley unit 2 (C)

Tvais=x(:,10);	% air temperature(C)

Rhvais=x(:,11);   % Relative Humidity (%)

Tsea=x(:,12);     % sea snake temperature(C)

The columns for files WHOTS_2012_proc_licor7500_1min.txt are as follow:

jdy=x(:,1); 	       % Day-Of-Year at beginning of time average

Licor_H2O=x(:,2);        %  Specific humidity (g/kg)

Licor_CO2=x(:,3);        % Licor CO2 (umol/mol)

Licor_Tempi=x(:,4);      % Licor temperature (degC)

Licor_Pressi=x(:,5);     % Licor pressure (hPa)

Licor_agci=x(:,6);       % Livor AGC value (%)

The columns for files WHOTS_2012_proc_son_1min.txt are as follows:

jdy=x(:,1);     % Day-Of-Year at beginning of time average

U=x(:,2);       % Relative u wind component (+boward) , m/s

V=x(:,3);       % Relative v wind component (+portward) , m/s

W=x(:,4);       % Relative w wind component (+up) , m/s

Tsonic=x(:,5);  % sonic temperature, C

dir =x(:,6)     % Relative wind direction (from),clockwise relative to ship's bow, deg

The columns for files WHOTS_2012_proc_ gpsnav_1min.txt are as follow:

jdy=x(:,1); 	    % Day-Of-Year at beginning of time average

gpslat1i=x(:,2);      % decimal latitude, deg

gpslon1i=x(:,3);      % decimal longitude, deg

gpsspeedi=x(:,4);     % GPS SOG, m/s

gpsheadi=x(:,5);      % GPS COG, deg

headxi_pitch=x(:,6);  % Crescent GPS heading, deg

pitchxi_pitch=x(:,7); % Crescent GPS angle (pitch), deg

A second set of programs reads the daily 1-min text files; time matches the various data sources, averages them to 5 or 30 minutes, computes fluxes, and writes new daily flux files. The 5-min and 30-min daily flux files have been combined and rewritten as a single file to form the file WHOTS_2012_PSD_flux_5min_all.txt and WHOTS_2012_PSD_flux_30min_all.txt.

The column assignment for those files is as follow:

jdy=x(:,1); 	%Day-Of-Year at beginning of time average

s1t1=x(:,2);      %psd bow true wind speed, m/s

dir1t1=x(:,3);    %psd bow true wind direction, deg

ts=x(:,4);        %psd seasnake T, C

ts_tsg=x(:,5);    %ship thermosalinograph T, C  bow (NaN is not available)

sal_tsg=x(:,6);   %ship thermosalinograph salinity, psu  bow (NaN is not available)

ta=x(:,7);        %psd air T, C

qs=x(:,8);        %psd air specific humidity at sea surface, g/kg

qa=x(:,9);        %psd air specific humidity, g/kg

psp=x(:,10);      %psd solar flux, w/m^2

pir=x(:,11);      %psd IR flux, w/m^2

org=x(:,12);      %psd optical raingage precip rate, mm/hr

sogm5=x(:,13);    %SOG from gps, m/s

cogm5=x(:,14);    %COG from gps, deg

relsp1=x(:,15);   %relative bow wind speed, m/s

reldir1=x(:,16);  %relative bow wind direction, deg

lat=x(:,17);      %decimal latitude, deg

lon=x(:,18);      %decimal longtude, deg

zt=x(:,19);       %Depth of SST sensor used in heat flux calc, m

sig_sp=x(:,20);   %standard deviation of ship speed, m/s

taub=x(:,21);     %wind stress, coare 3.0, N/m^2

hsb=x(:,22);      %sensible heat flux, coare 3.0, w/m^2

hlb=x(:,23);      %latent heat flux, coare 3.0, w/m^2

rf=x(:,24);       %rain heat flux, w/m^2

ta_im=x(:,25);    %IMET air t, C  from RTD (NaN if not available)

qa_im=x(:,26);    %IMET air specific humidity from RTD, g/kg (NaN if not available)

s_shp1=x(:,27);   %ship port true wind speed, m/s (NaN if not available)

dir_shp1=x(:,28); %IMET port true wind direction, deg (NaN if not available)

psp_im=x(:,29);   %IMET solar flux, w/m^2 (NaN if not available)

pir_im=x(:,30);   %IMET IR flux, w/m^2 (NaN if not available)

pressm=x(:,31);   %Barometric pressure, mb

rh_psd=x(:,32);   %RH (%)

Finally, below are reference heights (with respect to water line) of the sensors used in the WHOTS2012 experiment.

| Sensor | Sampling rate | Height (m) |
| --- | --- | --- |
| Bow sonic | 10 Hz | 18.3 |
| Motion Pack | 10 Hz | 17.5 |
| ORG | 0.1Hz, averaged to 1 sample/min | 16.6 |
| T/RH | 1Hz | 16.0 |
| Licor (CO2&H2O) | 10 Hz | 16.9 |
| Radiometers (top wheelhouse) | 0.1Hz, averaged to 1 sample/min | 15 |
| Barometer | 0.1Hz, averaged to 1 sample/min | 14 |
| SST | 0.1Hz, averaged to 1 sample/min | -0.05 to -0.10 |

Table 1.1. PSD sensor heights and sampling rates.